## Slide 1: Hand Arm Vibration
Date

## Slide 2: Who is affected?
Over Five Million
Two Million
300,000
workers are exposed to vibration at work
workers are at serious risk of developing HAVS
workers are showing advanced HAVS symptoms

## Slide 3: But first a word on competence
Construction is a dangerous industry and improving competence is key to reducing accidents. It is people that often cause accidents.
Competence is skills, knowledge and behaviour.
Competence is thinking about:
Self-awareness: get to know yourself
Situational awareness: expect the unexpected
Risk awareness: think outside the box

## Slide 4: Self-awareness: get to know yourself
Think about YOURSELF and your role
Consider your frame of mind
Late nights and hang-overs can affect judgement
Domestic disputes and emotional upsets affect concentration
All these can affect performance and safety

## Slide 5: Situational awareness: expect the unexpected
Don’t assume today will be the same as yesterday - things change.
Take note of the broader context in which you work
Stop and think about what’s going on around you
Things change so expect the unexpected risk

## Slide 6: Risk awareness: Think outside the box
Risk awareness is more than risk assessment. It recognises the additional risks of:
Age
Inexperience
Poor eyesight
Fading light
Language
Consider out-of-context risk due to new jobs and unfamiliar surroundings

## Slide 7: Hand Arm Vibration
Stops you doing the simplest things:
Turning pages of a paper
Picking up small items
Fastening buttons
Tying shoelaces
Zipping up your trousers!

## Slide 8: Meet the symptoms
Pins and needles
Loss of sense of touch
Severe pain and numbness
Fingers turn white
Loss of grip strength

## Slide 9: How to identify the risk
Look for measurement – metres per second squared (m/s²)
The higher the number the higher the vibration
The higher the number the less time the machine can be used
Use these numbers to compare machines

## Slide 10: How to control exposure
Don’t use vibrating tools if at all possible
If in doubt, shout – ask your supervisor
Well maintained machines and sharp tools work faster
Do not ‘force’ the machine
Work rotation – anti-vibration PPE
Use a Vibration Monitoring System
Remember YOU matter. Protect YOURSELF
Vibration Management System

## Slide 11: Do you have any choice?
What the law says EMPLOYERS have to do:
“All employers shall take action to control and reduce exposure, provide information, instruction, training and regular health checks.”
What the law says EMPLOYEES have to do:
“ All employees shall take all reasonable steps to ensure that they comply with safety procedures, training and operating guidelines set out by the employer.”
Did you know?
Health Surveillance must be provided for employees who are regularly above the EAV.

## Slide 12: Controlling exposure
JCB with Breaker Attachment
Concrete and Steel Nailer
Heavy Duty Road Breaker – Petrol
Cut-off Saw
Diamond Drilling Rig

## Slide 13: What you should do
Select the best tool and consumables for the job
Use tools correctly
Keep your hands warm and dry
Know the symptoms and keep looking for them
Report any symptoms

## Slide 14: Summary
Competence is key – it’s skills, knowledge and behaviour
Think differently about vibrating equipment
There is NO safe level of vibration
It’s about avoiding long-term pain and permanent disability
Know the symptoms and report any sign of them

## Slide 15: Quick quiz
Competence requires skills and knowledge and what else?
What are the three human factors we need to focus on to improve competence?
What are the regulations that cover hand arm vibration?
What are the symptoms of HAVs?
How many people suffer from HAVs?
What does m/s² stand for?
According to the HSE what should a good roadbreaker measure in m/s²?
Is there a safe level of vibration?
How can you reduce exposure to vibration?
Which products can help you reduce exposure?
Remember you are responsible for your safety and that of your mates