## Slide 1: GET A HEAD FOR HEIGHTS

## Slide 2: Falls from height – the facts
Falls from height remain the main cause of fatal workplace accidents in 2022/23

## Slide 3: Falls from height – the facts
Places and activities where falls occur: -
Ladders and steps: 40%
Vehicle beds/FLT forks : 17%
Machinery/plant maintenance: 10%
Platforms inc MEWPs: 10%
Stairs (see below): 8%
Roof/false ceiling: 7%
Scaffold/gantry: 4%
Warehouse racking: 4%

## Slide 4: Defining competency
Construction is the highest fall from height risk
Competence is key to reducing accidents
Human factors are the main contributor to falls from height
Competence is defined as skill, knowledge, experience and attitude
Think about situational awareness, self-awareness and risk awareness

## Slide 5: Self awareness
Always consider your role and capability
Take into account your frame of mind
General health and medication drugs and alcohol on the day after!
Emotional wellbeing
All effect performance, awareness and safety

## Slide 6: Situational awareness
Don’t assume things will remain the same, sites and associated risks continually change
STOP…….think and organise before proceeding
Consider other trades working in the same environment

## Slide 7: Risk awareness
Contribute to risk assessment relevant to you
Consider additional risks
Age
Experience, or lack of
Visibility
Complete point of work (dynamic) risk assessments on the job

## Slide 8: Work at Height Regulations
Six principles
  Apply to everyone
  Require risk assessment
  Select the right equipment
  Use equipment correctly
  Competency and planning
  Collective responsibility

## Slide 9: Apply to everyone, every where
All employees, Sub-contractors and self employed
In offices, on-site, warehouses, shops etc
At any height, above or below ground

## Slide 10: Risk Assessment
Avoid working at height where possible
Prevent falls with collective measures wherever practicable, e.g. handrails
Avoid ladders and steps if possible (only use for very short durations maintaining 3 points of contact
Minimise the consequences of a fall, e.g. fall arrest, soft landing bags

## Slide 11: Equipment selection

## Slide 12: Equipment use

## Slide 13: Planning and competency
All work at height should be planned and organised
Equipment must be used correctly in line with manufacturer’s instructions
Anyone working at height should be trained and competent
Never assume competence and …….if in doubt STOP the job and seek advice

## Slide 14: Collective responsibility
You have duties and responsibilities when working at height
Look out for others working in the vicinity
Report any hazards to a site supervisor and ensure appropriate control measure are implemented

## Slide 15: Summary
Work at height regulations (2005) principles
Apply to everyone
Require risk assessment
Select the right equipment
Use equipment correctly
Competency and planning
Collective responsibility
Competency is key, skill, knowledge, experience and attitude

## Slide 16: Quick quiz
Competence requires skills and knowledge and what else?
What are the three human factors we need to focus on to improve competence?
What are the regulations that cover working at height?
Can you name three of the six principles that make up the regulations?
Who does the regulations apply to and at what height?
What are the three stages of risk assessment?
What are the safe alternatives to ladders and steps?
It OK for anyone to erect a tower?
Do you have a legal obligation to implement the regulations?
What products could help you when working at height?
Remember you are responsible for your safety and that of your mates